## Slide 1: Forth on COR24
Three Forth kernels for a 24-bit soft CPU: all assembly, Forth-in-Forth, and Forth on a Forth-shaped substrate
: SQUARE DUP * ;
ok
5 SQUARE .
25 ok
sw-embed · October 2026 · sw-embed.github.io/web-sw-cor24-forth
Notes: Deck covers the COR24 target and its ISA limits, the three Forth implementations in sw-cor24-forth, how they compare with other Forths, the demo set in the web UI, and the everyday workflow of defining, listing, running and redefining words.

## Slide 2: What this deck covers
1
The target
COR24 in one page, and what its ISA takes away from a Forth writer.
2
Three implementations
forth.s, forth-in-forth and forth-on-forthish: what each keeps in assembly and why. Plus forth.s hosted inside SWTOS.
3
Choices vs. other Forths
Threading, cell size, HERE semantics, division, dictionary search.
4
The demos
What each dropdown entry teaches, which tabs run it, and the hardware demos.
5
Working with words
Define, run, list, inspect, redefine and forget, in the web UI and on the CLI.

## Slide 3: The target: COR24
A 24-bit RISC soft CPU for Lattice MachXO FPGAs (makerlisp.com)

## Slide 4: COR24 at a glance
24-bit
registers, addresses and cells; one cell is 3 bytes
32
opcodes in 211 forms; instructions are 1, 2 or 4 bytes
1
condition flag (C), set by ceq / clu / cls, tested by brt / brf
Register | Role in the Forth kernels
r0 | W: work register, holds the fetched CFA
r1 | RSP: return stack pointer, SRAM 0x0F0000 growing down
r2 | IP: threaded-code instruction pointer
sp | DSP: data stack, hardware push / pop into 3 KB EBR, starts 0xFEEC00
fp | scratch; the only register that can index the EBR stack
z, iv, ir | hardwired zero; interrupt vector and return
Address | Device
0x000000 | 1 MB SRAM: kernel, dictionary, return stack
0xFEE000 | 3 KB EBR block RAM: the hardware data stack
0xFF0000 | LED D2 (write) and switch S2 (read), same pin, active-low
0xFF0100 / 01 | UART data and status (bit 0 RX ready, bit 7 TX busy)

## Slide 5: What the ISA takes away from a Forth writer
r
Only r0, r1, r2 take results
Loads and ALU results never land in fp or sp. There is no mov r0, sp: reading the stack pointer is mov fp, sp; push fp; pop r0. DEPTH and .S pay that dance.
±
Branches reach ±127 bytes
Anything farther is la r0, label; jmp (r0): 5 bytes and a clobbered W. The colon-word entry template therefore comes in a 3-byte near and a 6-byte far form.
r1
jal links through r1
r1 is the return stack pointer, so the kernels never use call / return. Every primitive ends in an inlined NEXT and all nesting goes through the Forth return stack.
÷
mul, but no divide
/MOD is repeated subtraction: assembly on forth.s, a Forth loop on forth-on-forthish. Printing a number with . is the most expensive thing a demo does.
8
8-bit immediates, decimal only
la costs 4 bytes and is the only way to reach I/O: la r0, -65280 for the UART. No string literals, no .align; names are .byte lists padded by hand.
!
A 3 KB data stack that halts
About 1,000 cells. The emulator stops the CPU on overflow, so a word that leaks one cell per loop turn kills a demo after ~500 turns. That exact bug shipped once (see Demos).

## Slide 6: Design shared by all three kernels
Direct-threaded code: NEXT is 3 instructions, 5 bytes, inlined at the tail of every primitive
lw r0, 0(r2) ; W = mem[IP] (fetch CFA)
add r2, 3 ; IP += one cell
jmp (r0) ; run the primitive
Dictionary entry: a singly linked list, newest first
link 3 bytes previous entry, 0 ends the chain
flags_len 1 byte bit7 IMMEDIATE, bit6 HIDDEN, len
name N bytes no terminator
CFA 3 or 6 B near/far DOCOL template,
or the primitive's own code
Registers are frozen across kernels: r0 = W, r1 = RSP in SRAM, r2 = IP, sp = DSP in EBR.
HERE, LATEST, STATE and BASE push the variable's address, so Forth code writes HERE @. Unusual (JonesForth does it, ANS does not) but it keeps ! writes trivial.
No loader: the kernel boots straight into QUIT and everything else, including core/*.fth, arrives as UART text, exactly as if typed.
The outer loop echoes ok after every clean line and ? after an unknown token; a stack underflow prints a message and returns to the prompt.
FIND walks the link chain on forth.s; tabs 2 and 3 add a 256-bucket first-character hash in front of the walk.

## Slide 7: Choices compared with other popular Forths
Aspect | COR24 Forth | JonesForth | eForth | gforth
Threading | DTC, inlined NEXT | ITC | ITC or subroutine | DTC / ITC / token
Cell | 24-bit (3 bytes) | 32-bit | 16 / 32-bit | 32 / 64-bit
Kernel source | asm, down to ~22 prims + Forth | x86 asm + Forth | ~30 prims + Forth | C + Forth
Standard | pragmatic subset | subset | mostly ANS | Forth-2012
HERE | variable (HERE @) | variable (HERE @) | value | value
Division | repeated subtraction | hardware idiv | Forth-coded UM/MOD | C / hardware
Dictionary lookup | link walk + first-char hash | link walk | link walk, vocabularies | hashed
I/O model | memory-mapped UART, LED, switch | Linux syscalls | serial port | host OS, files
Numbers | signed 24-bit, BASE; no floats | 32-bit, no floats | 16 / 32-bit | floats, doubles
Deliberately missing: floating point, strings beyond EMIT, blocks, vocabularies, exceptions. Each would cost assembly the board does not need.

## Slide 8: Three implementations
in · in-ish · from: how much of the kernel is Forth

## Slide 9: One language, three kernels (and a fourth under way)
1
forth.s
All-assembly kernel
3,498
lines of asm
0
lines of Forth core
~65
primitives
Tab 1: the debugger. Canonical kernel for the FPGA board and the reg-rs golden tests.
2
forth-in-forth
Forth runs in a slimmed asm host
2,720
lines of asm
276
lines in 4 core tiers
50
primitives, 61 colon words
Tab 2: self-hosting REPL. IF, ., WORDS, SEE are Forth.
3
forth-on-forthish
Forth on a Forth-ish substrate
2,659
lines of asm (see note)
497
lines in 5 core tiers
~22
irreducible primitives, 82 colon words
Tab 3 (default): :, WORD, FIND, NUMBER, INTERPRET, QUIT are Forth.
4 forth-from-forth (phase 4, in progress): a cross-compiler written in Forth emits the kernel .s, so no hand-written assembly remains. Retargeting becomes a new asm-emit module.

## Slide 10: forth.s: the all-assembly kernel (tab 1)
Generated: forth-core.s (target-independent DTC Forth) + forth-uart.s (UART at 0xFF0100, return stack at 0x0F0000, halting BYE). The layer contract is what lets SWTOS host the same core (next slide).
Every word is assembly, including IF / THEN, ., WORDS, \ and (. ~65 primitives, 3,879 bytes assembled.
Richest vocabulary: FORGET, :NONAME, DO / ?DO / LOOP / I / UNLOOP, CONSTANT, VARIABLE, AGAIN / WHILE / REPEAT, DEPTH, .S.
Fastest: the Fibonacci demo compiles and runs in about 40 M instructions.
It is what runs on the physical board and what the reg-rs golden-output suite is baselined against, so it changes slowly.
In the web UI it backs the debugger: step, step-over, breakpoints, registers, both stacks and memory, with the UART pump feeding input between steps.
A primitive, end to end: LED!
entry_led_store:
.word entry_immediate ; link
.byte 4 ; len
.byte 76, 69, 68, 33 ; "LED!"
do_led_store:
add r1, -3
sw r2, 0(r1) ; save IP
pop r0 ; n
lcu r2, 1
and r0, r2 ; low bit
la r2, -65536 ; 0xFF0000
sb r0, 0(r2)
lw r2, 0(r1)
add r1, 3
lw r0, 0(r2) ; NEXT
add r2, 3
jmp (r0)
Note the saved IP: even a leaf primitive spills r2 because pop and la need a second register.

## Slide 11: The same core inside SWTOS: Forth as a pane
One core, two layers
forth-core.s dictionary, inner + outer interpreter, every primitive; never touches hardware
forth-uart.s
UART at 0xFF0100, return stack at 0x0F0000, BYE halts
= forth.s, tab 1 and the board
forth-swtos.s (sw-tos)
I/O via kernel services into its own pane; 8 KB dictionary and 1 KB return stack in the module; BYE or Escape exits the process
; the contract, end of forth-core.s
layer_init io_emit io_key io_bye
io_branch io_zbranch dict_start layer_latest
; sw-tos vendors the core with
scripts/vendor-forth-core.sh --check
Live: swtos.softwarewrighter.com/forth/ boots SWTOS's forth profile in the browser. At the shell type bg forth; the REPL opens in its own pane.
Four layer words: MENU lists the 18 vendored examples, n LOAD runs one as if typed, n LIST prints it, RESET forgets everything. Words are case-insensitive.
It is a resident program like any other: its data stack is the process stack (256 cells), and a Forth loop that never yields (example 21, HOG) is preempted by the clock and can be killed from the shell. On the bare kernel that loop needs a reset.
Nothing in the core changed to make this work. The split into forth-core.s plus a layer was done so SWTOS could own I/O, stacks and exit while the Forth stays byte-identical.
Same source commit as tab 1, so the three web tabs and the SWTOS pane run the same Forth; only the host differs.

## Slide 12: forth-in-forth: Forth extends itself (tab 2)
minimal.fth
IF THEN ELSE BEGIN UNTIL AGAIN WHILE REPEAT, = 0=, \ and (, :NONAME
lowlevel.fth
NIP TUCK ROT PICK 2DUP 2SWAP 1+ 1- NEGATE ABS / MOD, CONSTANT VARIABLE, DO ?DO LOOP
midlevel.fth
CR SPACE HEX DECIMAL and the number printer .
highlevel.fth
DEPTH .S ' WORDS VER >NAME SEE SEE-CFA DUMP-ALL
Each tier uses only primitives and the tiers before it. The kernel streams them in over UART at boot, so WORDS shows them as ordinary colon definitions.
Control flow is four lines of Forth
: IF ['] 0BRANCH , HERE @ 0 , ; IMMEDIATE
: THEN HERE @ OVER - SWAP ! ; IMMEDIATE
: BEGIN HERE @ ; IMMEDIATE
: UNTIL ['] 0BRANCH , HERE @ - , ; IMMEDIATE
Three new primitives made it possible: ['] (compile a named CFA), EOL! (let a Forth \ end the line) and SP@ (for DEPTH and .S).
18 words left assembly; 19 new ones appeared. Kernel 2,983 lines to 2,239 at the time, binary 28% smaller.
SEE decompiles any colon word, including IF itself.
Cost: compile-time words run as threaded code. Fibonacci needs ~120 M instructions instead of 40 M; runtime of compiled code is unchanged.

## Slide 13: forth-on-forthish: a Forth-shaped substrate (tab 3)
Group | What stays in assembly
Threading | NEXT, DOCOL, EXIT, LIT, BRANCH, 0BRANCH, EXECUTE
Memory | @ ! C@ C!
Arithmetic | + and NAND (AND, OR, XOR, INVERT, NEGATE, - are derived)
Stack pointers | SP@ SP! RP@ RP! (DUP, SWAP, OVER become memory ops)
I/O | KEY EMIT LED! SW?
Compile | HERE LATEST STATE BASE, ,DOCOL (emits the 6-byte CFA template)
Hand-off | QUIT-VECTOR: the CFA of the Forth QUIT once highlevel.fth has loaded
: DUP SP@ @ ;
: DROP SP@ 3 + SP! ;
: INVERT DUP NAND ;
: AND NAND INVERT ;
: - NEGATE + ;
: : CREATE ,DOCOL ... ] ;
: ; ['] EXIT , ... 0 STATE ! ; IMMEDIATE
Even : and ; are colon definitions. The only help is ,DOCOL, which copies the COR24 opcode bytes Forth cannot encode itself.
WORD, FIND, NUMBER, INTERPRET and QUIT are Forth. After the last core line installs QUIT-VECTOR, every prompt line runs through Forth code.
Honest number: kernel.s is still 2,659 lines. The asm bootstrap must compile runtime.fth before Forth : exists, so the asm WORD / FIND / NUMBER bodies stay alive. Deleting them needs a precompiled image: that is phase 4.
Cost: Fibonacci needs an 800 M instruction budget; stack ops via SP@ are several times slower than push / pop.

## Slide 14: Boot: one kernel binary, then a stream of text
cor24-asm
kernel.s → .lgo
CPU resets,
_start → QUIT
core/*.fth tiers
arrive over UART
“ok” prompt
demo, upload
or typed line
Tab 1 sends no core files and is interactive at once. Tab 2 streams four tiers, tab 3 five. The same bytes work on the CLI:
cor24-asm forth-on-forthish/kernel.s -o kernel.lgo
cor24-emu --lgo kernel.lgo --speed 0 -n 800000000 \
-u "$(cat forth-on-forthish/core/*.fth examples/14-fib.fth)"
In the browser a pump hands bytes to the UART only while the PC sits in one of the kernel's known poll loops, in sub-batches of 2 k instructions, then lets compile work run in 50 k batches.
Those poll-loop labels are the one thing a new kernel must register; a headless test boots all three kernels through the pump to catch a missing one.
Fibonacci demo | Instructions | Why
forth.s | ~40 M | everything native
forth-in-forth | ~120 M | IF / UNTIL compile as threaded code
forth-on-forthish | ~800 M budget | WORD / FIND / NUMBER and stack ops in Forth

## Slide 15: Trade-offs between the three
 | forth.s | forth-in-forth | forth-on-forthish
Speed | fastest; compile and run native | runtime same; compile ~3× slower | everything through Forth; ~20× the budget
Assembly to maintain | ~3,500 lines, every word | ~2,700 lines, 50 primitives | ~2,650 lines, but only ~22 matter after boot
What SEE can show | no SEE | IF, ., WORDS as Forth | also :, WORD, FIND, INTERPRET
Retarget to a new CPU | rewrite everything | rewrite 50 primitives + bootstrap | rewrite ~22 primitives + bootstrap; outer interpreter is portable Forth
Extra vocabulary | FORGET, :NONAME | SEE, DUMP-ALL, PICK, ROT | NAND, SP!, RP@, RP!, WORD-BUFFER
Bootstrap risk | none | tier order matters | chicken-and-egg: asm loop must compile Forth : first
Best for | the board, debugging, golden tests | learning how Forth defines itself | porting; seeing the whole interpreter as Forth

## Slide 16: The demos
The dropdown in every tab, backed by sw-cor24-forth/examples/*.fth

## Slide 17: Language demos: what each one teaches
Demo | File | Teaches | Tabs
Smoke Test | 00 | .S, arithmetic, HEX, WORDS: interpret mode only | 1 2 3
Colon Definitions | 01 | TWO, SQUARE, CUBE: compile mode and nesting | 1 2 3
Math Words | 03 | NEGATE, DOUBLE, TRIPLE, * | 1 2 3
ASCII Stars | 04 | EMIT patterns from composed words | 1 2 3
Comments | 06 | \ line comments and ( ) inline comments | 1 2 3
Division & Modulo | 07 | /MOD, then / and MOD built from it | 1 2 3
IF THEN / IF ELSE | 08 09 | conditional execution inside a definition | 1 2 3
Loop | 10 | BEGIN UNTIL counting up and down | 1 2 3
FizzBuzz | 11 | nested IF ELSE inside BEGIN UNTIL, 1 to 20 | 1 2 3
Fibonacci (manual / looped) | 14 | defines its own NIP TUCK 1+ 1-; FIB(0)..FIB(10) or ..FIB(20) | 1 2 3
AGAIN / WHILE REPEAT | 15 16 | BEGIN AGAIN with IF EXIT; test-in-middle TRIANGLE sum | 2 3
CONSTANT / VARIABLE | 17 18 | named values; a COUNTER cell with BUMP / RESET / SHOW | 2 3
DO LOOP | 19 | DO ?DO I UNLOOP, factorial, early EXIT | 2 3
SEE (all words) | inline | defines SQUARE and CUBE, then DUMP-ALL decompiles every word | 2 3
Self Test | 12 | every kernel word; stack empty at the end; intentional ? ? errors | 1 2 3
Also in examples/, upload as .fth: 20-redefine (shadowing, FORGET), 21-hog (never yields), 22-factorial (recursion), 23-bases.

## Slide 18: Hardware demos: S2 in, D2 out
S2
D2
0xFF0000 bit 0
read: 0 = pressed
write: 0 = LED on
1
LED Control (02)
: ON 1 LED! ; : OFF 0 LED! ;
Then ON, OFF, BLINK. Watch the red dot. Because the pin is active-low, 0 LED! is the one that lights it.
2
Switch → LED (05)
SW? LED! one shot: click S2 first, then Run. The raw bit is copied straight through, so pressed (0) lights D2.
3
Loop Switch LED (13)
MIRROR polls SW? LED! 16,000 times with two delay loops between reads. Toggle S2 while it runs and D2 follows within a tick.
The regression, and the tests that now guard it
April 2026: the delay loops leaked two cells per turn; the 3 KB stack overflowed after ~500 turns and the halted CPU looked like a dead LED.
Web: tests/led_switch_demo.rs boots each kernel headlessly, presses S2 mid-run and asserts D2 follows and the stack does not drift.
CLI: cor24-emu --switch-at 6000000:on,8000000:off logs [S2 @ N] and [LED @ N] lines for reg-rs golden tests.

## Slide 19: Define, run, list, redefine
Define
: SQUARE ( n -- n*n ) DUP * ;
ok
Colon opens a definition, semicolon closes it. A word can call itself by name (recursion). Definitions live until Reset.
Run
5 SQUARE .
25 ok
Type the word and press Enter; ↑ ↓ recall history. Demos: pick one, click Run. Your own file: Upload .fth. Stop pauses; Reset reboots and forgets everything.
List and inspect
WORDS \ newest first
SEE SQUARE \ tabs 2 and 3: DUP * ;
DUMP-ALL \ every word with address
1 2 .S DEPTH .
WORDS on every tab; SEE, SEE-CFA, DUMP-ALL and ' need the Forth-defined kernels.
Redefine, edit, forget
: GREET 72 EMIT 105 EMIT ;
: TWICE GREET GREET ;
: GREET 72 EMIT 101 EMIT 121 EMIT ; \ shadows
TWICE \ old GREET, twice
FORGET GREET \ forth.s only
A new definition sits in front of the old one; earlier callers keep the binding they compiled. To edit: fix the source, then FORGET (forth.s) or Reset and re-run the file.

## Slide 20: Known quirks and open items
!
forth-on-forthish rejects negative literals
Its Forth NUMBER has no sign handling, so -1 and -65280 print ?. CONSTANT, DO LOOP, IF THEN, IF ELSE and Self Test fail on tab 3; the headless test pins them as known-broken until fixed.
0
LED! and SW? are raw active-low bits
0 LED! lights D2 and SW? returns 0 while pressed. The Help text still says non-zero on and -1 pressed; one of the two should change.
F
FORGET exists only on forth.s
Tabs 2 and 3 redefine by shadowing; reclaiming dictionary space means Reset.
T
Test suite drift
The reg-rs suite in sw-cor24-forth still names the retired cor24-run binary; the two new switch tests use cor24-asm + cor24-emu. The web help doc test lists 12 kernel words with no reference entry.

## Slide 21: Try it
sw-embed.github.io/web-sw-cor24-forth (three kernels, press ? for the guide) · swtos.softwarewrighter.com/forth/ (forth.s as an SWTOS pane: bg forth)
Repositories, all under github.com/sw-embed
Web UI
web-sw-cor24-forth
Kernels and demos
sw-cor24-forth
Emulator and CLI
sw-cor24-emulator
Assembler
sw-cor24-x-assembler
SWTOS and its web demo
sw-tos, web-sw-tos
Board
makerlisp.com